## Slide 1
Curved-Head Teapot Blueprint
Target: 4.0 cups (946 ml)
Estimated Capacity: 946 ml
Overall Height: 149.3 mm (5.88 in)
Body Max Dia: 100.1 mm (3.94 in)
Head Top Dia: 129.5 mm (5.10 in)
Material Baseline: Stainless Steel 304 + nylon handle + silicone gasket
Design Notes
- Images indicate a multi-part stainless vessel with a separate curved upper head.
- Material suggestions are generated from reflectivity, color distribution, and repeated part visibility.
- For stainless manufacturing, 304 is selected as baseline; 316L remains optional for higher corrosion resistance.

## Slide 2
Material Suggestions
Part | Selected Material | Recommended | Confidence | Notes
Lower vessel body shell | Stainless Steel 304 (0.9 mm) | Stainless Steel 304 (0.9 mm) | 86% | Deep-draw + spin forming friendly and food safe.
Curved upper head / funnel section | Stainless Steel 304 (0.9 mm) | Stainless Steel 304 (0.9 mm) | 83% | Spin form and trim rolled lip for curved head profile.
External handle | Glass-filled Nylon 66, heat-resistant | Glass-filled Nylon 66, heat-resistant | 61% | Thermal isolation from vessel body.
Center insert / filter collar | Stainless Steel 304 + 80 mesh screen | Stainless Steel 304 + 80 mesh screen | 80% | Keeps tea leaves from pouring path.
Sealing ring / gasket | Food-grade Silicone (Shore A 50-60) | Food-grade Silicone (Shore A 50-60) | 33% | Compensates tolerance stack and seals head/body interface.
Bottom cap / base ring | Stainless Steel 304 (1.0 mm) | Stainless Steel 304 (1.0 mm) | 76% | Reinforces base and protects seam edge.

## Slide 3
Manufacturing Bill of Materials
Part | Material | Process | Thk (mm) | Qty | Mass (g)
Lower vessel body shell | Stainless Steel 304 (0.9 mm) | Deep draw + neck reduction + brushing | 0.78 | 1 | 198.5
Curved upper head / funnel section | Stainless Steel 304 (0.9 mm) | Spin forming + lip trim | 0.78 | 1 | 96.1
Center insert / filter collar | Stainless Steel 304 + 80 mesh screen | Stamp + draw + mesh spot weld | 0.62 | 1 | 22.1
External handle | Glass-filled Nylon 66, heat-resistant | Injection mold + fastener insert | 12.09 | 1 | 21.5
Sealing ring / gasket | Food-grade Silicone (Shore A 50-60) | Compression mold | 2.59 | 1 | 1.4
Bottom cap / base ring | Stainless Steel 304 (1.0 mm) | Stamp + trim | 1.00 | 1 | 35.8